Isparta Volkanik Zemini Çökme Potansiyeli

Collapse Potential of Isparta Vulcanic Soils

Mahmut MUTLUTÜRK*, Tevfik İSMAİLOV*, Vijdan BALCI**

* Süleyman Demirel Üniversitesi Mühendislik Mimarlık Fakültesi Jeoloji Mühendisliği Bölümü

**Jemas Ltd. Şti.Ankara

mutlu@mmf.sdu.edu.tr

ÖZ

Çökme lös ve lös benzeri zeminlerde görülen bir deformasyon çeşididir. Bünyesine su alan zemin, kendi ağırlığı yada ilave yük etkisi ile daneler arasındaki bağın hızlı bir şekilde bozulması ile çöker. Çökmeye neden olan ana etken, zeminin yüksek boşluk oranına bağlı boşluklu dokusu ve düşük kuru birim hacim ağırlığıdır. Doygun hale gelen bir zeminin çökmeye eğiliminin olup olmadığı nispi çökme katsayısı (εSL) ve hangi basınç altında çökmeye başlayabileceği gösteren başlangıç çökme basıncı (PSL) ile belirlenmektedir. Laboratuvarda örselenmemiş numunelerden yapılan deneysel çalışmalar ile belirlenen εSL ve PSL çökme potansiyelinin belirlenmesinde önemli göstergeleri oluşturmaktadır.

Isparta ovasında yer alan silt ve siltli kum özelliğindeki volkanik zeminlerin bazı seviyeleri yüksek boşluk oranı (e=0.74-0.86) ve düşük kuru birim hacim ağırlıkları (γd=13.4-14.1 kN/m3) ile çökme davranışı gösterebilecek bir dokuya sahiptir. Bu nedenle, Isparta Ovası volkanik zeminlerinin çökme potansiyeli araştırma konusu olarak seçilmiştir.

Yapılan çalışmada, volkanik zeminlerin siltli kum seviyelerinden alınan örselenmemiş numuneler kullanılmıştır. Deneysel çalışmalarda oedometre yardımı ile tek ve çift eğri yöntemi kullanılarak εSL ve PSL belirlenmeye çalışılmıştır. Numunelerin oedometre cihazında doğal, doygun ve 300 kPa kadar doğal ve 300 kPa dan sonra doyurularak yüklemeleri üç set halinde yapılmıştır. Deneysel çalışma sonuçlarına göre Isparta ovası volkanik zeminlerinin 300 kPa basınç için 0.01 < εSL < 0.06 Zayıf Çöken Zemin, başlangıç çökme basıncının 80 < PSL < 100 kPa olduğu belirlenmiştir. Bu sonuçlara göre, Isparta Ovası volkanik zeminlerinin zayıf çökme potansiyeline sahip olduğu ve 80 kPa nın üzerindeki basınçlarda doygun hale gelmesi halinde çökme davranışı gösterebileceği anlaşılmıştır.

Anahtar Kelimeler: Çökme potansiyeli, volkanik zemin

ABSTRACT

Collapse is a kind of deformation which is seen in loess and loess like soils. Soil which absorbs water collapses with its own weight or extra load with fast break down of tie between particles. The main reason for collapse is porous textures with high void ratios and relatively low dry densities. Determination of lean to collapse of saturated soil has been performed by using coefficient of relative collapse (εSL) and initial collapse pressure (PSL) which is the point of starting collapse pressure. εSL and PSL which are determined with experiments carried out in the laboratory with undisturbed samples are important indicators to determine collapse potential.

Some levels of volcanic soils which look like silt and sand with silt in Isparta Plain with high void  ratio (e=0.74-0.86) and low dry density (γd=13.4-14.1 kN/m3) has a texture of collapse behavior. Therefore, collapse potential of Isparta Plain has been chosen as a research subject in this study.

In this study, samples which are collected from sand levels with silt of volcanic soils are used. εSL and PSL values are determined by using single and dual curve method with odometer in experimental studies. Samples are loaded to odometer in three sets as natural, saturated, natural until 300 kPa and saturated after 300 kPa. According to results of experimental studies, it is determined that Isparta Plain volcanic soils are weak collapse soils for 300 kPa with 0.01 <εSL< 0.06 and initial collapse pressure of 80 < PSL <100 kPa. Therefore, Isparta Plain volcanic soils have weak collapse potential and it is seen that they will show a collapse behavior after pressure of 80 kPa if they are saturated.

Keywords: Collapse potential, vulcanic soil

Değinilen Belgeler

Abalev, Yu. M. and. Abalev, M. Yu.,1968.  Fundamentals of design and Construction on Macroporous Soils Prone to Slump-type Settlement (in Russian), Stroiizdat, Moscow.

Aliyev, S.K., 1966. Başlangıç basıncın ve deformasyon bölgenin çöken temel zeminlerde belirlenme metodu. Azerbaycan politeknik enstitü ilmi teknik dergisi No 2(8), Seri 10, 1966.

ASTM D-2435, 2003. Standard test method for one-dimentional consolidation properties of soils using incremental loading.

ASTM D-4333, 1992. Standard test method for measurement of collapse potential of soils.

Clevenger, W.A., 1958. Experience with loess as foundation material. Proceedings American Society Civil Engineers, Journal Soil Mechanics Foundations Division, 85, 151-180.

Denisov, N.Ya., 1953. Construction properties of loess and loess-like ground. Gostudarstvennoe Izd, Moscow, second ed. 154p. (first ed. 1951, 136p.) (in Russian).

Dudley, J.G., 1970. Review of collapsing soils. The journal of Soil Mechanics and Foundation Division ASCE 96, 925-947.

Feda, J., 1988. Collapse of loess upon wetting. Engineering Geology, Volume 25, Issues 2-4, 263-269.

Fookes, P.G. and Best, R., 1969. Consolidation characteristics of some late Pleistocene periglacial metastable soils of east Kent. Quarterly Journal Engineering Geology, 2, 103-128.

Gibss, H.H. and Bara, J.P., 1962. Predicting surface subsidence from basic soil tests. American Society Testing Materials (ASTM), Special Technical Publication, No. 322, 231-246.

Kriger, N.I., 1965. Loess-its Characteristics and Relation to the Geographical Environment. Nauka, Moscow, 296p. (in Russian; bibliography republished as Loess Letter Supplement 13, July 1986).

Kurutov, V.I., 1972. Foundations on Soils Prone to Slump-type Settlement (in Russian), Stroiizdat, Moscow.

Musrafaev, A..A., 1978. Foundamentals of the Mechanics of Soils Prone to Slump-type Settlement (in Russian), Stroiizdat, Moscow.

Norms and Technical Specifications for the Design and Construction of Buildings and Industrial Structures on Macroporous Soils Prone to Slump-type Settlement, Norm and Technical Specification 137-56 (in Russian), Stroiizdat, Moscow (1956).

Reznik, Y.M., 1994. Evaluation of collapse potentials using single oedometer test results. Bulletin of the Association of Engineering Geologists XXXI (2), 255-261.

Reznik, Y.M., 2000. Engineering approach to interpretation of oedometer tests performed on collapsible soils. Engineering Geology, Volume xx, Issue 57. 205-213.

Tsytovic, N.A., 1973. Soil Mechanics. (2th Edition) Vysshaya Shkola, Moscow, (in Russian).

Balcı, V.,2007. Hızırbey Mahallesi 8101 Ada, 155 Parsel Temel Zemini Çökme Deformasyonu Özelliklerinin İncelenmesi. SDÜ, Jeoloji Mühendisliği Bölümü, Bitirme Ödevi (Yayımlanmamış),